## Slide 1: Switching Theory and Logic Design (STLD)
Theory - ETEC-205
B. Tech – 3rd Sem
August 2020 – January 2021
Faculty: Ms. Anubha Goel

## Slide 2: STLD Lesson Plan

## Slide 3: Outline of the lecture
Combinational circuits
  Half adder
  Full adder
  Half subtractor
  Full subtractor
  binary Parallel adder
  Binary adder-subtractor
  Bcd adder
  Serial adder
  Look ahead carry adder

## Slide 4: Combinational circuits
Combination logic circuits are the circuits whose outputs depend upon on the present input combination
  The previous inputs or outputs do not alter the present outputs
  They do not have memory
They can be represented by Boolean functions
Combinational circuit comprises of input variables, logic gates and output variables
  Inputs and outputs are binary in nature i.e. can only take 0 or 1 as the possible values
‘n’ input variables
‘m’ output variables
Combinational logic circuit

## Slide 5: Combinational circuits
Designing Procedure for combinational logic circuits will follow the steps as:
  Input variables and output variables are identified and assigned distinct letter symbols
  Truth table is derived, which states value of each output for all possible input combinations
  Simplified Boolean expression is obtained for each output variable, either by K-map or Boolean algebra
  Logic circuit is drawn using desired logic gates
Things to remember
  ‘n’ input variable will have 2n input combination, therefore number of rows in truth table will be 2n
  For the system having ‘n’ input variables and ‘m’ output variables, the number of columns in truth table will be ‘n+m’

## Slide 6: Combinational circuits
Combinational circuits that we need to study
  Code Convertors
  Adders
  Subtractors
  Magnitude Comparators
  Parity bit Generators
  Encoders and Decoders
  Multiplexers and De-multiplexers

## Slide 7: Half adder
Combinational circuit that performs arithmetic addition
Follows the rules of binary addition
The inputs are two binary bits, addend ‘A’ and augend ‘B’
The outputs are a sum bit ‘S’ and a carry bit ‘C’
The truth table for half adder (HA) with two inputs (A,B) and two outputs (S,C) is
Inputs |  | Outputs | 
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 8: Half adder
By minimizing using K-map, the reduced relations for Sum and Carry bits are obtained as
  Sum (S) = A’B +AB’ = A (XOR) B
  Carry (C) = AB

## Slide 9: Half adder
The combinational circuit for half adder can be realized using
  one XOR gate to calculate Sum (S) and
  one AND gate to calculate Carry (C)

## Slide 10: full adder
Combinational circuit that performs arithmetic addition
Follows the rules of binary addition
Half adder can add only two bits at a time, no provision to add carry generated from previous bit addition. To resolve this, full adder circuit is designed
There are three inputs each of one bit: addend ‘A’, augend ‘B’ and carry from previous bit addition called carry-in ‘Cin’ i.e. [A + B + Cin]
The outputs are a sum bit ‘S’ and a carry bit called carry-out ‘Cout’.
This carry bit, Cout, is propagated to next significant bit for subsequent addition or provided as the output

## Slide 11: full adder
The truth table for full adder (FA) with three inputs (A,B, Cin) and two outputs (S,Cout) is
Inputs |  |  | Outputs | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 12: full adder
By minimizing using K-map, the reduced relations for Sum and Carry-out bits are obtained as
Sum (S)
= A’B’Cin + A’BCin’ + AB’Cin’ + ABCin
= A (XOR) B (XOR) Cin
Carry-out (Cout)
= AB + BCin + ACin
Carry-out (Cout) can also be written as
= A’BCin + AB’Cin + ABCin’ + ABCin
= Cin [A (XOR) B] + AB

## Slide 13: full adder
The combinational circuit for full adder can be realized using
  two XOR gates to calculate Sum (S) and
  two AND gates and one OR gate to calculate Carry-out (Cout)

## Slide 14: full adder
The full adder can also be realized using two half adders and an OR gate

## Slide 15: Half subtractor
Combinational circuit that subtracts one bit from another
Follows the rules of binary subtraction
The inputs are two binary bits, minuend ‘X’ and subtrahend ‘Y’ i.e. [X-Y]
The outputs are a Difference bit ‘D’ and a Borrow bit ‘B’
The truth table for half subtractor (HS) with two inputs (X,Y) and two outputs (D,B) is
Inputs |  | Outputs | 
X | Y | D | B
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
X
Y
D
B
Half Subtractor

## Slide 16: Half subtractor
By minimizing using K-map, the reduced relations for Difference and Borrow bits are obtained as
  Difference (D) = X’Y +XY’ = X (XOR) Y
  Borrow (B) = X’.Y

## Slide 17: Half subtractor
The combinational circuit for half subtractor can be realized using
  one XOR gate to calculate Difference (D) and
  one AND gate and one NOT gate to calculate Borrow (B)

## Slide 18: full subtractor
Combinational circuit that performs arithmetic subtraction
Follows the rules of binary subtraction
Like half adder, half subtractor can also subtract only two bits at a time. It cannot subtract borrow generated from previous bit subtraction. To resolve this, full subtractor circuit is designed
There are three inputs each of one bit: minuend ‘X’, subtrahend ‘Y’ and borrow from previous bit subtraction called borrow-in ‘Bin’ i.e. [X-Y-Bin]
The outputs are a Difference bit ‘D’ and a borrow bit called carry-out ‘Bout’.
This borrow bit, Bout, is propagated to next significant bit for subsequent subtraction or provided as the output
X
Y
D
Bout
Full Subtractor
Bin

## Slide 19: full subtractor
The truth table for full subtractor (FS) with three inputs (X,Y, Bin) and two outputs (D, Bout) is
Inputs |  |  | Outputs | 
X | Y | Bin | D | Bout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 20: full subtractor
Using K-map, the reduced relations for D and Bout are obtained as
Difference (D) = X’Y’Bin + XYBin + X’YBin’ + XY’Bin’
= X (XOR) Y (XOR) Bin
Borrow-out(Bout) = X’Y + X’Bin + YBin
Borrow-out (Bout) can also be written as
= X’Y’Bin + XYBin + X’YBin + X’YBin’
= Bin [X (XOR) Y]’ + X’Y

## Slide 21: full subtractor
The combinational circuit for full subtractor can be realized using
  two XOR gates to calculate Difference (D) and
  two AND gates, two NOT gates and one OR gate to calculate Borrow-out (Bout)

## Slide 22: full subtractor
The full subtractor (FS) can also be realized using two half subtractors (HS) and an OR gate

## Slide 23: binary Parallel adder
Binary Parallel adder performs addition of two ‘n-bit’ binary numbers, addend A and augend B, in parallel
n-bit addition requires ‘n’ Full-adders
  Addition of Least significant bits (LSBs) of A and B can be done by either by a half-adder or a full-adder
  Full adders are connected in chain
  The Cout of each full-adder is connected to Cin of next higher order full-adder
Addition generates the sum bits as parallel outputs
  Addition of two 4-bit numbers, A3A2A1A0 and B3B2B1B0, will result in sum S3S2S1S0 and final output carry (generated after addition of A3 and B3)
  Will require 4 Full-adders cascaded such that Cout of FA0 is connected to Cin of FA1 , Cout of FA1 is connected to Cin of FA2 and so on
Also called as RIPPLE CARRY ADDER

## Slide 24: binary Parallel adder
Addition of two 4-bit numbers, A3A2A1A0 and B3B2B1B0, requires 4 full-adders
Outputs are 4-bit Sum S3S2S1S0 and a final output carry (C4) due to addition of bits A3 and B3
All the respective bits of A and B are added simultaneously to generate the sum bit and carry for next bit position

## Slide 25: Binary adder―subtractor
Subtraction of two binary numbers can be performed using Binary Parallel Adder
Adding 2’s complement of subtrahend to minuend is equivalent to subtracting subtrahend from minuend
  A − B = A + (2’s complement of B)
2’s complement of B is obtained using
  inverters to calculate 1’s complement
  Then adding ‘1’ at LSB through carry-in (Cin) of Binary parallel adder
A common circuit called binary adder―subtractor can perform both addition and subtraction of two binary numbers
  Exclusive – OR gates are included at input of each full-adder circuit to convert the binary parallel adder into binary adder-subtractor circuit

## Slide 26: Binary adder―subtractor
  This circuit performs addition or subtraction of two 4-bit numbers, A (A3A2A1A0) and B (B3B2B1B0).Output will be 4-bit Sum (S3S2S1S0) and output carry, C4
MODE input ‘M’ controls the binary operation to be performed. ‘B’ is Ex-ORed with ‘M’ and provided as an input to full-adder
M = 0 → B (XOR) M = B (XOR) 0 = B
  FAs have inputs A, B, and Cin (=0). The circuit works as a Binary Adder
M = 1 → B (XOR) M = B (XOR) 1 = B’
  FAs have inputs A, B’, and Cin (=1)
  B’ and Cin=1, together forms 2’s complement of B. The circuit works as a Binary Subtractor. [A-B = A+(2’s complement of B)]

## Slide 27: serial adder
Serial Adder adds bits of two binary numbers in serial order
Only one pair of bits are added at a time, therefore only one Full-adder is required for addition of addend (A) and augend (B)
Input bits are stored in registers and shifted out, one bit at a time, as inputs to the full adder
Addition of serial input bits start from the LSBs (A0, B0) then (A1, B1) and so on till MSBs.
Output Carry (Cout) bit generated from any one addition is saved in a flip-flop and provided as input carry (Cin) to next higher order bit addition
Output sum is stored in a register
Serial adders are slower than parallel adders, as only one bit is added per clock pulse
They are used where circuit minimization is more important than speed

## Slide 28: serial adder
Addend (A) and augend (B) are stored in separate registers
Output sum (S) can either be stored in separate register or in same as any of the input

## Slide 29: bcd adder
BCD (Binary Coded Decimal) codes or 8421 codes comprises of 4-bit binary representation for decimal digits 0,1,2,3,4,5,6,7,8 and 9 (0000 to 1001)
BCD Adder is the combinational circuit that adds two BCD digits and the sum is also a valid BCD number
The addend and augend are BCD numbers, means each can have any value from 0 (0000) to 9 (1001). Hence, the sum can range only from 0 to 18
Maximum sum that can be obtained by adding two BCD digits is 19, when there in a carry-in from previous digit addition (A + B + Cin = 9 + 9 + 1).
Till the Sum is less than or equal to 9 (1001), it can be represented by corresponding single BCD digit. But, for sum in range of 10 to 19, it is represented by two BCD digits i.e. 10 is (0001 0000);15 is (0001 0101);19 is (0001 1001)

## Slide 30: bcd adder
BCD adder circuit comprises of a correction circuit to detect and perform the required conversion of sum from non-valid BCD value to valid BCD value
The steps for performing BCD addition are
  Add the two 4-bit BCD digits using binary parallel adder
  For the positions where the sum is equal to or less than 9, the sum is a valid BCD number and therefore, no correction is required
  For the positions where the sum is greater than 9 and less than or equal to 19, the sum is a non-valid BCD number. Therefore, the correction is required
Correction is done by adding binary 6 (0110) to the obtained sum. Adding ‘6’ maps the binary sum to its equivalent valid BCD number. An output carry (C) is also produced for next digit addition
The necessary condition that should be ‘TRUE’ or ‘1’ for the correction circuit to operate is calculated from the truth table that maps Binary sum into the equivalent BCD sum

## Slide 31: bcd adder
Truth table for mapping Binary sum (KZ8Z4Z2Z1) to BCD sum(CS8S4S2S1). The correction is required when
Output carry in Binary Sum (K) =1
Z8 is 1 and either of Z4 and Z2 is 1 → Z8 Z4 + Z8 Z2 = 1
Hence, C = K + Z8 Z4 + Z8 Z2 has to be 1 for 6 (0110) to be added

## Slide 32: bcd adder
BCD adder comprises of two 4-bit binary adder circuits
First binary adder adds Addend and Augend, with input carry, Cin to generate Binary sum (KZ8Z4Z2Z1)
Using K, Z8, Z4 and Z2, value of output carry (C) is calculated
  If C = 0, then nothing is added to binary sum. The BCD sum is same as binary sum
  If C = 1, then binary 0110 is added to binary sum through second binary adder. The binary sum is mapped to equivalent BCD sum with output carry (C) as 1

## Slide 33: Look ahead carry adder
In Parallel adder, the speed of addition is controlled by the time required by the carry inputs to propagate through all the FAs
All the addend and augend bits are already loaded to each FA, but the sum bit can only be calculated after the value of carry-in is propagated and available for addition
In a 4-bit parallel adder, the total propagation time taken by the carry-out to propagate will be time taken in eight logic gates
For n-bit parallel adder, propagation time for carry-out is ‘2n’ gate levels, hence, the limiting factor for the speed

## Slide 34: Look ahead carry adder
LOOK AHEAD CARRY adder speeds up the addition by reducing the propagation delay time
All the input bits are examined simultaneously and carry-in bits, for all stages, are also generated simultaneously
Two additional functions are incorporated in this adder to speed up the addition process
  Carry Generate(Gi): provides the output carry when both A and B are ‘1’, irrespective of value of carry-in (Ci)
  Gi = Ai.Bi
  Carry propagate (Pi): function associated with the propagation of carry from Ci to Ci+1
  Pi = Ai (XOR) Bi
  Sum and Carry-out are
  Si = Pi (XOR) Ci
  Ci+1 = Gi + Pi.Ci
  where i=0,1,..,3, denotes the bit position being added in FA and the stage in parallel adder

## Slide 35: Look ahead carry adder
Using equation for carry-out (Ci) of each stage
Ci+1 = Gi + Pi.Ci
The equation for carry-out of each full-adder becomes
C1 = G0 + P0.C0
C2 = G1 + P1.C1
C3 = G2 + P2.C2
Cout = C4 = G3 + P3.C3
Substituting the values of Ci in these, we get
C1 = G0 + P0C0
C2 = G1 + P1C1
= G1 + P1 (G0 + P0C0)
= G1 + P1G0 + P1P0C0
C3 = G2 + P2.C2
= G2 + P2 (G1 + P1G0 + P1 P0C0)
= G2 + P2G1 + P2P1G0 + P2P1 P0C0

## Slide 36: Look ahead carry adder
It is evident from the equations of C1, C2 and C3, that only one level of AND gate followed by an OR gate will generate each carry-out
Generation of C3 does not require C2 and C1 to get propagated (as in case of Parallel adder). They all are propagated at the same time
Logic expressions for each ‘Ci’ in look ahead carry generator:
C1= G0 + P0C0
C2= G1 + P1G0 + P1 P0C0
C3=G2 +P2G1 +P2P1G0+P2P1 P0C0

## Slide 37: Look ahead carry adder
For all i = {0,1,2,3}, Pi is generated by an XOR gate and Gi by an AND gate
Carries are propagated through look ahead carry generator and provided as inputs to second XOR gates
All output carries are generated after delay of two levels of gates
Each Sum bit requires only two XOR gates
Sums S0 – S3 are generated with equal propagation delays

## Slide 38: Problems (TBD)
TBD