## Slide 1: Switching Theory and Logic Design (STLD)
Theory - ETEC-205
B. Tech – 3rd Sem
August 2020 – January 2021
Faculty: Ms. Anubha Goel

## Slide 2: STLD Lesson Plan

## Slide 3: Outline of the lecture
Combinational circuits
  Magnitude comparator
  Parity generator
  Decoder
  Encoder
    Priority encoder
  Multiplexer
  Demultiplexer

## Slide 4: magnitude comparator
Combinational circuit that compares the magnitude of two binary numbers, A and B, to determine whether (A > B), (A < B) or (A = B)
For two 4-bit numbers, A (A3A2A1A0) and B (B3B2B1B0), there are three possible cases
CASE 1: [A = B]
  If and only if all pairs of corresponding bits are equal, i.e. A3 =B3 and A2 =B2 and A1 =B1 and A0 =B0
  This equality can be represented by a logic function
  xi = AiBi +Ai’Bi’ for i = 0,1,2,3
  ‘xi’ = 1, if bits at ith position are equal, i.e. if both are 1 or both are 0
  For A=B, all ‘xi’ should be 1, indicating AND of all xi
  Therefore, [A = B] = x3 x2 x1 x0

## Slide 5: magnitude comparator
Determining whether (A > B) or (A < B), requires comparison of magnitudes of pairs of corresponding bits
Comparison of numbers, A (A3A2A1A0) and B (B3B2B1B0) start from the most significant bit (MSB) position. If both are equal, them next lower significant pair bits are compared
Comparison is done till a pair of unequal bits is obtained
Among the unequal pair, if
  Corresponding digit of A is ‘1’ and B is ‘0’, then A > B
  Corresponding digit of A is ‘0’ and B is ‘1’, then A < B

## Slide 6: magnitude comparator
CASE 2 : [A > B]
  If (A3 = 1 & B3 = 0)
  If A3 = B3 and (A2 = 1 & B2 = 0)
  If A3 = B3 , A2 = B2 and (A1 = 1 & B1 = 0)
  If A3 = B3 , A2 = B2 , A1 = B1 and (A0 = 1 & B0 = 0)
This inequality can be represented by a logic function
  [A > B] = A3B3’ + x3 A2B2’ + x3 x2 A1B1’ + x3 x2 x1 A0B0’
CASE 3 : [A < B]
  If (A3 = 0 & B3 = 1)
  If A3 = B3 and (A2 = 0 & B2 = 1)
  If A3 = B3 , A2 = B2 and (A1 = 0 & B1 = 1)
  If A3 = B3 , A2 = B2 , A1 = B1 and (A0 = 0 & B0 = 1)
This inequality can be represented by a logic function
  [A < B] = A3’B3 + x3 A2’B2 + x3 x2 A1’B1 + x3 x2 x1 A0’B0
[A=B], [A>B] and [A<B] are considered the output variables of the magnitude comparator, which equals to logic ‘1’ or HIGH, according to the magnitudes of A and B

## Slide 7: magnitude comparator

## Slide 8: magnitude comparator
The logic circuit of magnitude comparator
NOR gates to check the equality and hence, calculate ‘xi’
AND, OR and NOT gates to check Inequality

## Slide 9: PARITY GENERATOR and checker
PARITY bit is an extra bit which is used for the purpose of error detection
While transmitting the binary message, parity bit is attached with the message bits such that the count of number of 1’s is either odd or even
The receiver counts the number of 1’s in the received data and detects an error by checking the parity
Parity check can detect only single bit errors
At the transmitter end, the circuit that generates parity bit is called Parity Generator
At the receiver end, the circuit that checks the parity is called Parity Checker
According to the number of 1’s, there are classified as
  EVEN parity - the total number of 1’s in the transmitted data (binary message including parity bit) is even
  ODD parity - the total number of 1’s in the transmitted data (binary message including parity bit) is odd

## Slide 10: PARITY GENERATOR and checker
EVEN-PARITY GENERATOR
Parity bit is added at the beginning or at the end of the message
The EVEN parity bit (P) for 4-bit message signal D3D2D1D0, is generated by counting number of 1’s in D3D2D1D0
  P=1, if the count of 1’s in the 4-bit input is odd (such that the count of 1’s in the 4-bit input and parity bit together is even)
  P=0, if the count of 1’s in the 4-bit input is even
4-BIT MESSAGE |  |  |  | PARITY BIT
D3 | D2 | D1 | D0 | P
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 11: PARITY GENERATOR and checker
EVEN-PARITY GENERATOR
By truth table the equation for output parity bit (P) is obtained as
P = D3 (XOR) D2 (XOR) D1 (XOR) D0
The logic circuit for even parity generator requires 3 XOR gates

## Slide 12: PARITY GENERATOR and checker
PARITY CHECKER
At the receiver occurrence of an error is reported, if
  the number of 1’s are even in an odd parity system or
  the number of 1’s are odd in even parity system
To check the error, all the bits in the received data are XORed to give an output ERROR (E).
  If E=1, then there is an error
  If E=0, then there is no error during the transmission
4-BIT MESSAGE PARITY BIT |  |  |  |  | ERROR BIT
D3 | D2 | D1 | D0 | P | E
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0

## Slide 13: PARITY GENERATOR and checker
EVEN-PARITY CHECKER
The equation for output error bit (E) is obtained as
E = D3 (XOR) D2 (XOR) D1 (XOR) D0 (XOR) P
The logic circuit for even parity generator requires 4 XOR gates

## Slide 14: Decoder
Combinational circuit that converts ‘n’ binary input line code into ‘m’ output lines is called a DECODER
For ‘n’ input lines, there are 2n possible input combination. For each possible input combination only one output line is active, hence m is equal to 2n
Referred as n:m or n-to-m line decoder, where m = 2n
Few are 1:2, 2:4, 3:8, 4:16 and so on
There may/may not be an additional control input called ENABLE
  If HIGH or ‘1’ will provide the output according to input code
  If LOW or ‘0’ will force all the outputs to be LOW irrespective of the input combination
‘n’
input lines
‘m= 2n’
output lines
n:m
DECODER

## Slide 15: Decoder
3:8 or 3-to-8 line decoder
Three input lines are decoded into 8 output lines
Each output line represents one of the eight possible minterms
Inputs |  |  | Outputs |  |  |  |  |  |  | 
x | y | z | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 16: Decoder
3:8 or 3-to-8 line decoder
According to the minterm represented by each output line, they can be also realized by logically ANDing the input variables x, y and z,

## Slide 17: Decoder
A larger order decoders can be realized using multiple smaller order decoders
The ENABLE input is used to select among the multiple smaller decoders
ENABLE input is enabled (= HIGH or ‘1’) or disabled (= LOW or ‘0’), according to the input combinations/minterms that are to be generated
3:8 decoder using 2 × 2:4 decoders
Inputs |  |  | Outputs |  |  |  |  |  |  | 
A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 18: Decoder
4:16 decoder:
There will be 4 Input lines and 16 output lines.
Depending upon the input combination, only one of the 16 lines will be HIGH.
Inputs |  |  |  | Outputs |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | D8 | D9 | D10 | D11 | D12 | D13 | D14 | D15
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 19: Decoder
4:16 decoder using 2 × 3:8 decoders
4:16 decoder using 5 × 2:4 decoders

## Slide 20: Decoder
(EXAMPLE 1)
Realize full adder circuit using one 3:8 decoder
The output equations of Full Adder are:
SUM (S) = f(A, B, Cin) = ∑ (1,2,4,7)
CARRY-OUT (Cout) = f(A, B, Cin) = ∑ (3,5,6,7)

## Slide 21: encoder
Combinational circuit that perform inverse operation of a Decoder
It converts ‘m’ binary input line code into ‘n’ output lines, where m = 2n
For each of the 2n input lines, the output corresponding to its binary value is generated
Only one input line can be HIGH or ‘1’ at a particular time
Referred as m:n or m-to-n encoder, where m = 2n
Few are 2:1, 4:2, 8:3, 16:4 and so on
‘m= 2n’
input lines
‘n’
output lines
m:n
ENCODER

## Slide 22: encoder
8:3 encoder
Also referred as octal-to-binary encoder
Eight input lines are encoded into its equivalent 3-bit binary value, represented by 3 output lines
Inputs |  |  |  |  |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | x | y | z
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
The output equations are:
x = D4 + D5 + D6+ D7
y = D2 + D3 + D6+ D7
z = D1 + D3 + D5+ D7

## Slide 23: encoder
8:3 encoder
According to the input line being represented by each output line, 8:3 encoder can also be realized using OR gates for the input lines D0 – D7

## Slide 24: encoder
10:4 encoder or Decimal-to-BCD encoder
Ten input lines are there (one for each decimal digit), each is encoded into its corresponding 4-bit BCD code, represented by 4 output lines
Decimal Inputs | Outputs |  |  | 
 | Y3 | Y2 | Y1 | Y0
D0 | 0 | 0 | 0 | 0
D1 | 0 | 0 | 0 | 1
D2 | 0 | 0 | 1 | 0
D3 | 0 | 0 | 1 | 1
D4 | 0 | 1 | 0 | 0
D5 | 0 | 1 | 0 | 1
D6 | 0 | 1 | 1 | 0
D7 | 0 | 1 | 1 | 1
D8 | 1 | 0 | 0 | 0
D9 | 1 | 0 | 0 | 1
The output equations are:
Y3 = D8 + D9
Y2 = D4 + D5 + D6+ D7
Y1 = D2 + D3 + D6+ D7
Y0 = D1 + D3 + D5 + D7 + D9

## Slide 25: PRIORITY encoder
PRIORITY ENCODER: Encoder that includes priority function
It calculates the output when two or more inputs are equal to ‘1’ at the same time
The output is obtained according to the input which is having the highest priority
In a 4:2 priority encoder, among the 4 inputs, the order of priority is: Y3 > Y2 > Y1 > Y0
In a ‘m : n’ priority encoder, the output equivalent to an input line can be obtained only and only if,
  all the other high priority inputs are ‘0’
  irrespective of the values of other lower priority input lines

## Slide 26: PRIORITY encoder
The working of priority encoder is
  Y3 has highest priority: If ‘Y3 = 1’ the output will be A1A0= 11, regardless of values of Y2, Y1 and Y0,
  Y2 is next in precedence order: If ‘Y2 = 1’ then the output A1A0= 10, if and only if ‘Y3 = 0’ regardless of values of Y1, and Y0
  Similarly, for ‘Y1 = 1’ the output is A1A0= 01; and for ‘Y0 = 1’ the output is A1A0= 00, only if all the higher priority inputs are ‘0’
Inputs |  |  |  | Outputs |  | 
Y0 | Y1 | Y2 | Y3 | A1 | A0 | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1
An additional output, ‘Valid’ or ‘V’ is used to indicate that multiple input lines that are ‘1’
  V=1, if one or more inputs are ‘1’
  V=0, if all inputs are ‘0’
The ‘X’ in truth table signifies the don’t care combination

## Slide 27: PRIORITY encoder
From the truth table, the equation for A1, A0 and V can be derived in terms of input variables Y3, Y2, Y1 and Y0
The input combinations with ‘X’ can take both values ‘1’ or ‘0’, so all the possible minterms are considered for minimizing using K-maps
The equations for output lines are:
A1 = Y2 + Y3
A0 = Y3 + Y2’ Y1
V = Y3 + Y2 + Y1+ Y0

## Slide 28: multiplexer
MULTIPLEXER: Combinational circuit that selects binary information from many input lines and directs it to the single output line, called MANY-to-ONE device
There will one and only one output line
Selection of input line is directed by additional control input lines called Select lines
  For selecting among ‘n’ input lines, the number of select line required are ‘m’, where n = 2m
  The binary combination decides which input is to be connected with output
Referred as n:1 multiplexer or n:1 MUX, with m select lines. Few are 2:1(m=1), 4:1(m=2), 8:1(m=3), 16:1(m=4) and so on
‘n’
input lines
‘one’
output lines
n:1 MUX
‘m’
select lines

## Slide 29: multiplexer
4:1 MUX:
4 inputs, 1 output, 2 select lines
According to select lines, S1-S0, input line will be connected to output line
  S1S0=00, output Y= D0
  S1S0=01, output Y= D1
  S1S0=10, output Y= D2
  S1S0=11, output Y= D3
The value of input (0 or 1), will be provided as the output, Y
Select Inputs |  | Outputs
S1 | S0 | Y
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3

## Slide 30: multiplexer
4:1 MUX:
The logic diagram of MUX is realized using basic gates
The output equation is:
Y = S1’S 0’ D0 + S1’S0D1 + S1S0’D2 + S1S0D3

## Slide 31: multiplexer
8:1 MUX:
8 inputs, 1 output, 3 select lines
Binary combination of S2S1S0 directs the input being connected to Y
Select Inputs |  |  | Output
S2 | S1 | S0 | Y
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7

## Slide 32: multiplexer
A larger order multiplexer can be realized using multiple smaller order multiplexers
8:1 MUX using 2 × 4:1 MUX
Select Inputs |  |  | Output
S2 | S1 | S0 | Y
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7

## Slide 33: MULTIPLEXER
16:1 MUX using 8:1 MUX
Inputs |  |  |  | Outputs
S3 | S2 | S1 | S0 | Y
0 | 0 | 0 | 0 | I0
0 | 0 | 0 | 1 | I1
0 | 0 | 1 | 0 | I2
0 | 0 | 1 | 1 | I3
0 | 1 | 0 | 0 | I4
0 | 1 | 0 | 1 | I5
0 | 1 | 1 | 0 | I6
0 | 1 | 1 | 1 | I7
1 | 0 | 0 | 0 | I8
1 | 0 | 0 | 1 | I9
1 | 0 | 1 | 0 | I10
1 | 0 | 1 | 1 | I11
1 | 1 | 0 | 0 | I12
1 | 1 | 0 | 1 | I13
1 | 1 | 1 | 0 | I14
1 | 1 | 1 | 1 | I15

## Slide 34: MULTIPLEXER
16:1 MUX using 5 × 4:1 MUX
Inputs |  |  |  | Outputs
S3 | S2 | S1 | S0 | Y
0 | 0 | 0 | 0 | I0
0 | 0 | 0 | 1 | I1
0 | 0 | 1 | 0 | I2
0 | 0 | 1 | 1 | I3
0 | 1 | 0 | 0 | I4
0 | 1 | 0 | 1 | I5
0 | 1 | 1 | 0 | I6
0 | 1 | 1 | 1 | I7
1 | 0 | 0 | 0 | I8
1 | 0 | 0 | 1 | I9
1 | 0 | 1 | 0 | I10
1 | 0 | 1 | 1 | I11
1 | 1 | 0 | 0 | I12
1 | 1 | 0 | 1 | I13
1 | 1 | 1 | 0 | I14
1 | 1 | 1 | 1 | I15

## Slide 35: multiplexer
Higher-order MUX using single next lower-order MUX
Instead of multiple lower-order MUX, single lower-order MUX is used
For realization of ‘n’ variables function, ‘n-1’ variables are directly connected as select lines and the last variable is connected to the 2(n-1) input lines
The output function is evaluated such that it can be connected to the input lines of the MUX as either 0,1, the last variable or the complement of the last variable
  E.g. Realization of F(x,y,z) using one 4:1 MUX, will have ‘x’ and ‘y’ connected to select lines and ‘z’ as four input lines of 4:1

## Slide 36: multiplexer
Higher-order MUX using single next lower-order MUX
(EXAMPLE 1)
8:1 MUX using one 4:1 MUX
e.g Realize F(x,y,z) =∑ (1,2,6,7) using only one 4:1 MUX
Select Inputs |  |  | Output | 
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = z’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 

## Slide 37: multiplexer
Higher-order MUX using single next lower-order MUX
(EXAMPLE 2)
8:1 MUX using one 4:1 MUX
e.g Realize F(A,B,C) =∑ (0,1,2,5) using only one 4:1 MUX
Select Inputs |  |  | Output | 
A | B | C | F | 
0 | 0 | 0 | 1 | F = 1
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = C’
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = C
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | F = 0
1 | 1 | 1 | 0 | 

## Slide 38: multiplexer
Higher-order MUX using single next lower-order MUX
(EXAMPLE 3)
8:1 MUX using one 4:1 MUX
e.g Realize F(x,y,z) =∑ (1,4,5,6) using only one 4:1 MUX
Select Inputs |  |  | Output | 
x | y | z | F | 
0 | 0 | 0 | 0 | F = z
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | F = 0
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | F = 1
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | F = z’
1 | 1 | 1 | 0 | 

## Slide 39: multiplexer
Higher-order MUX using single next lower-order MUX
(EXAMPLE 4)
8:1 MUX using one 4:1 MUX
e.g Realize Carry-out of Full Adder using only one 4:1 MUX
Select Inputs |  |  | Output | 
A | B | Cin | Cout | 
0 | 0 | 0 | 0 | F = 0
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | F = Cin
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | F = Cin
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 

## Slide 40: multiplexer
Higher-order MUX using single next lower-order MUX (EXAMPLE 5)
16:1 MUX using one 8:1 MUX
Inputs |  |  |  | Outputs | 
A | B | C | D | F | 
0 | 0 | 0 | 0 | 0 | F = D
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 0 | F = D
0 | 0 | 1 | 1 | 1 | 
0 | 1 | 0 | 0 | 1 | F = D’
0 | 1 | 0 | 1 | 0 | 
0 | 1 | 1 | 0 | 0 | F = 0
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 0 | F = 0
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | F = D
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | F = 1
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 1 | 
                Realize F(A,B,C,D) = ∑(1,3,4,11,12,13,14,15) using only one 8:1 MUX
The Least Significant Bit (LSB) variable, ‘D’, is provided at the inputs of 8:1 MUX

## Slide 41: multiplexer
Higher-order MUX using single next lower-order MUX (EXAMPLE 6)
16:1 MUX using one 8:1 MUX
                Realize F(A,B,C,D) = ∑(2,4,5,7,10,14) using only one 8:1 MUX
                The LSB variable, ‘D’, is provided at the inputs of 8:1 MUX
Inputs |  |  |  | Outputs | 
A | B | C | D | F | 
0 | 0 | 0 | 0 | 0 | F = 0
0 | 0 | 0 | 1 | 0 | 
0 | 0 | 1 | 0 | 1 | F = D’
0 | 0 | 1 | 1 | 0 | 
0 | 1 | 0 | 0 | 1 | F = 1
0 | 1 | 0 | 1 | 1 | 
0 | 1 | 1 | 0 | 0 | F = D
0 | 1 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 0 | F = 0
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 1 | F = D’
1 | 0 | 1 | 1 | 0 | 
1 | 1 | 0 | 0 | 0 | F = 0
1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 0 | 1 | F = D’
1 | 1 | 1 | 1 | 0 | 

## Slide 42: multiplexer
Higher-order MUX using single next lower-order MUX (EXAMPLE 7)
16:1 MUX using one 8:1 MUX
                Realize F(A,B,C,D) = ∑(0,2,3,6,8,10,11,12,13,14) using only one 8:1 MUX
                The MSB variable, ‘A’, is provided at the inputs of 8:1 MUX
Inputs |  |  |  | Outputs
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 43: multiplexer
Higher-order MUX using single next lower-order MUX (EXAMPLE 8)
16:1 MUX using one 8:1 MUX
                Realize F(A,B,C,D) = ∑(0,1,2,4,6,9,12,14) using only one 8:1 MUX
                The MSB variable, ‘A’, is provided at the inputs of 8:1 MUX
Inputs |  |  |  | Outputs
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 44: De-multiplexer
DE-MULTIPLEXER: performs reverse operation of a MULTIPLEXER
Combinational circuit that takes binary information from a single input and directs it to one of the many output lines, called ONE-TO-MANY device
There will one and only one input line
Selection of output line is controlled by Select lines
  For selecting among ‘n’ output lines, the number of select line required are ‘m’, where n = 2m
  The binary combination decides the output line which will be connected with the input
Referred as 1:n de-multiplexer or 1:n DEMUX, with m select lines. Few are 1:2(m=1), 1:4(m=2), 1:8(m=3), 1:16(m=4), so on
‘one’
input line
‘many’
output lines
1:n DEMUX
‘m’
select lines

## Slide 45: DE-multiplexer
1:4 DEMUX:
1 input, 4 output, 2 select lines
According to select lines, S1-S0, input line will be connected to one of the output lines
  S1S0=00, output Y0 = Din
  S1S0=01, output Y1 = Din
  S1S0=10, output Y2 = Din
  S1S0=11, output Y3 = Din
The value of input (0 or 1), will be provided as the respective output, Y0-Y3
Select Inputs |  | Outputs |  |  | 
S1 | S0 | Y0 | Y1 | Y2 | Y3
0 | 0 | Din | 0 | 0 | 0
0 | 1 | 0 | Din | 0 | 0
1 | 0 | 0 | 0 | Din | 0
1 | 1 | 0 | 0 | 0 | Din

## Slide 46: DE-multiplexer
1:8 DEMUX:
1 input, 8 outputs, 3 select lines
Binary combination of S2S1S0 directs the input to either of the output lines, Y0-Y7
Select Inputs |  |  | Outputs |  |  |  |  |  |  | 
S2 | S1 | S0 | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
0 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | Din | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | Din | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Din

## Slide 47: DE-multiplexer
A larger order de-multiplexer can be realized using multiple smaller order de-multiplexers
1:8 DEMUX using 2 × 1:4 DEMUX
Select Inputs |  |  | Outputs |  |  |  |  |  |  | 
A | B | C | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
0 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | Din | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | Din | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Din

## Slide 48: De-MULTIPLEXER
1:16 DEMUX using 1:8 DEMUX
Inputs |  |  |  | Input (Din) available at Output
S3 | S2 | S1 | S0 | 
0 | 0 | 0 | 0 | Y0
0 | 0 | 0 | 1 | Y1
0 | 0 | 1 | 0 | Y2
0 | 0 | 1 | 1 | Y3
0 | 1 | 0 | 0 | Y4
0 | 1 | 0 | 1 | Y5
0 | 1 | 1 | 0 | Y6
0 | 1 | 1 | 1 | Y7
1 | 0 | 0 | 0 | Y8
1 | 0 | 0 | 1 | Y9
1 | 0 | 1 | 0 | Y10
1 | 0 | 1 | 1 | Y11
1 | 1 | 0 | 0 | Y12
1 | 1 | 0 | 1 | Y13
1 | 1 | 1 | 0 | Y14
1 | 1 | 1 | 1 | Y15

## Slide 49: Problems (TBD)